SECTION 07 41 13 – Metal Roof Panels

GENERAL

SUMMARY

Section Includes: Prefinished, prefabricated structural standing seam roof system with continuous interlocking field formed seams.

Related Requirements:

Section 05 10 00: Structural Metal Framing.

Section 05 40 00: Cold-Formed Metal Framing.

Section 05 50 00: Metal Fabrications.

Section 07 62 00: Sheet Metal Flashing and Trim

REFERENCES

Reference Standards:

ASTM A653: Steel Sheet, Zinc Coated (Galvanized) Class G90 by the Hot Dip Process.

ASTM E1680:  Rate of Air Leakage Through Exterior Metal Roof Panel Systems

ASTM E1592: Structural Performance of Sheet Metal Roof and Siding Systems by Uniform Static Air Pressure Difference.

ASTM E1646: Water Penetration of Exterior Metal Roof Panel Systems by Uniform Static Air Pressure Difference.

SMACNA Architectural Sheet Metal Manual.

UL 580: Standard for Tests for Uplift Resistance of Roof Assemblies

SUBMITTALS

Product Data.

Shop Drawings:

Indicate thickness and dimensions of parts, fastenings and anchoring methods, details and locations of joints, transitions and other provisions necessary for thermal expansion and contraction.

Indicate locations of field- and factory-applied sealant.

Samples:

Submit two samples, 12 inches long by full panel width, showing proposed metal thickness and seam profile.

Submit standard color samples of metal for Architect’s selection.

Manufacturer Qualifications.

Installer Qualifications: Submit list of completed projects, with names and contact information for architects and contractors.

Test Reports: Indicating compliance of products with project requirements.

Warranty Documentation.

Insurance Documentation.

QUALITY ASSURANCE

Manufacturer Qualifications:

Ten years' experience, minimum, in factory fabrication of metal panels.

Manufacturer shall carry $2,000,000 liability insurance, minimum, for metal panel system.

Installer Qualifications:

Three years' experience, minimum, in application of metal roof or wall panels.

Five satisfactory projects with metal panel work of similar scope and complexity to Work of this Project.

Installer must be approved by manufacturer, in writing, prior to bid.  Approval document must be included with project bid.

DELIVERY, STORAGE, AND HANDLING

Storage and Handling Requirements:

Keep panels and accessory items dry.

Protect against damage and discoloration.

Handle panels with non-marring slings.

Support panels to prevent permanent deformation.

Store panels above ground, with one end elevated for drainage.

Protect panels against standing water and condensation between adjacent surfaces.

If panels become wet, immediately separate sheets, wipe dry with clean cloth, and keep sheets separate for air-drying.

Painted panels shall be shipped with protective plastic sheeting or a strippable film coating between panels. Remove strippable film coating prior to installation. Do not allow strippable film coating to remain on panels in extreme heat, cold, or direct sunlight or other UV source.

Do not allow panels to contact treated lumber.

WARRANTY

Manufacturer's Warranty: Manufacturer’s standard 20-year performance warranty, stating the following:

Architectural fluorocarbon finish:

Will be free of fading or color change in excess of 5 Hunter delta-E units as determined by ASTM D2244-02.

Will not chalk in excess of numerical rating of 8 when measured in accordance with standard procedures specified in ASTM D4214-98 method D659.

Will not peel, crack, chip, or delaminate.

Metal substrate will not rupture, fail structurally, or perforate.

Installer's Warranty: Warrant panels, flashings, sealants, fasteners and accessories against defective materials and/or workmanship, covering repairs required to maintain roof panels watertight and weatherproof with normal usage for two years following Project Substantial Completion date.

Furnish written warranty, signed by installer.

Weathertight Performance Warranty:  Manufacturer's standard warranty in which manufacturer agrees to repair or replace metal roof panel assemblies that fail to remain weather tight within 2,5,10,15,20 Years from Date of Substantial Completion.

PRODUCTS

SYSTEM DESCRIPTION

Performance Criteria

Wind Uplift: Class 90 per UL 580

Panel system shall be ASTM E1592 tested under the supervision of an ANSI or ISO/IEC accredited laboratory and the laboratory shall issue the test report.

Air Infiltration: Tested in accordance with ASTM E1680.

0.022 cfm per linear foot of joint at static test pressure differential of 12.00 psf.

0.002 cfm per linear foot of joint at static test pressure differential of 12.00 psf.

Water Infiltration Under Static Pressure:  Tested with side lap sealant per ASTM E1646.

No leakage through panel joints at 15.00 psf.

No leakage through panel joints at 20.00 psf.

Water Penetration: No leakage through panel side seams and end laps when tested according to ASTM E1646

Thermal Movements: Accommodate thermal movement without buckling, joint opening, overstressing components, failure of connections, or other detrimental effects, through the following temperature changes:

120 degrees F, ambient.

180 degrees F, material surface.

PANELS

Products: Versa Span

Manufacture

Taylor Metal Products: 4566 Ridge Drive NE, Salem OR:

800-574-1388:Taylormetal.com

Panels: 1.75” Snap Seam Metal Roof Panel

Material: Steel

24 Gauge: minimum thickness of .0236”

Thickness and yield strength as required for performance indicated: ASTM A653: Steel Sheet, Zinc Coated (Galvanized) Class G90 by the Hot Dip Process. For projects with multiple profiles of varied combinations of profiles, rib patters and finishes, show on drawing.

Panel Width and Pattern: 18”.  With (Choose smooth or striated) pattern.

Panel Seam Height: 1.75”.

Panel Finish:

Polyvinylidine Fluoride, full 70 percent Kynar 500® consisting of a baked-on 0.15-0.20 mil corrosion resistant primer and a baked-on 0.70-0.80 mil finish coat with a specular gloss of 8 to 15 when tested in accordance with ASTM D523 at 60 degrees.

Color: Choose from full range of manufactures standard colors

Seam Sealant: Factory apply high-grade butyl mastic sealant within the confines of panel’s female leg, designed to seal against adjacent male panel leg.

FRAMING AND SUBSTRATES

Secondary Framing: See Section 05 40 00 "Cold-Formed Metal Framing".

Sheathing: See Section 06 16 00 "Sheathing".

Roofing Underlayment: As per Metal Roof Manufacturers recommendation.

CLIPS AND FASTENERS

Clips: Provide clip designed to allow panels to thermally expand and contract.

        - Fasteners: As recommended by manufacturer for performance indicated

INSULATION

Blanket insulation; See Section:  Insulation

ACCESSORIES

Trims and Flashings: Material, metal thickness, and finish to match panels. Profiles indicated in Drawings.

Provide manufacturer’s standard accessories and other items essential to completeness of standing seam roof installation.

Panel Penetration Flashings: As recommended by panel manufacturer; designed to provide sufficient movement to prevent creation of points of fixity at penetrations.

Sealant for Field Application: high grade non-curing butyl or curing urethane sealant as recommended by panel manufacturer.

FABRICATION

Fabrication, General:

Unless otherwise shown on Drawings or specified herein, fabricate panels in continuous lengths and fabricate flashings and accessories in longest practical lengths.

Panels:

Provide panels in full length from ridge to eave. Transverse seams not allowed.

Roof panels shall have flush horizontal and vertical surfaces to facilitate sealing at terminations. Panel configurations which create voids and requiring supplemental closure devices shall not be considered acceptable.

Engineer panels to use concealed anchors that permit expansion and contraction, except at eaves, end laps, ridges, valleys, hips and gables.

Seams:

Panel seams shall interlock entire length of seam.

Design standing seam to lock up and resist joint disengagement during design wind uplift conditions as calculated according to local building codes.

Provide pre-installed sealant within confines of panel’s female leg to aid in resistance of leaks and provide panel-to-panel seal while allowing expansion and contraction movement.

Seams shall be continuously locked or crimped together by mechanical means during installation. Seaming tools shall be sourced from manufacturer.

Fabrication Tolerances:

Flat metal surfaces will display waviness commonly referred to as “oil canning”. This is caused by steel mill tolerances and is a characteristic, not a defect, of panels manufactured from light gauge metal. Panels are factory correctively-leveled to minimize the occurrence of “oil canning”. As such, “oil canning” will not be accepted as cause for rejection.

EXECUTION

EXAMINATION

Verification of Conditions: With Installer present.

Examine conditions and substrates on which metal panels are to be installed. Structural support or substrate shall be flat and plumb to avoid panel stresses and distortion.

Prior to starting work, correct defects.

Field Measurements:

Coordinate field measurements and fabrication schedule with construction progress.

Field measure prior to fabrication. Show recorded dimensions on shop drawings, including locations of shop-fabricated openings.

If field measurements differ from drawing dimensions, notify Architect prior to fabrication.

INSTALLATION

Panels and Trim: Comply with manufacturer's instructions for assembly, installation and erection for weather tight installation.

Install according to approved shop drawings.

Install panels in accordance with manufacturer’s instructions and recommendations. Anchor securely in place using clips and fasteners spaced in accordance with manufacturer’s recommendations for design wind load criteria.

Form seams with manufacturer-approved motorized seaming tool; completely engage panel, clip, and factory-applied sealant in seam.

Comply with methods and recommendations of SMACNA Architectural Sheet Metal Manual for flashing configurations required.

Discrepancies between job site conditions and shop drawings shall be brought to the attention of the Architect for resolution.

Cutting and Fitting:

Cut panels neat, square, and true with shearing action cutters. Torch or power saw cutting is prohibited.

Openings 6 inches and larger: Shop fabricate and reinforce to maintain original load capacity.

Openings less than 6 inches: Field cutting is acceptable.

Dissimilar Metals or Materials:

Where panel or trim may come in contact with dissimilar metals or treated lumber, fabricate transition to facilitate drainage and minimize possibility of galvanic action.  Galvanic action can cause panels and trim to fail prematurely.

At points of contact with dissimilar metal or treated lumber, coat panel and trim with protective paint or separate materials with a weatherproof underlayment.

Direct contact or run-off from CCA, ACQ, CA, or other treated lumber (outdoor wood) or fire retardant impregnated or treated wood shakes or siding can cause panels and trim to fail prematurely.  Avoid contact with these materials.

Accessories: Install trims, flashings, and roofing specialties according to Drawings and manufacturer's recommended details.

Sealant Installation: Apply according to approved shop drawings and SMACNA Architectural Sheet Metal Manual recommendations.

Provide airtight and waterproof installation.

CLEANING

Repairs:

Touch up paint is not required for panels with scratches that do not expose metal.

Panels or flashings with finish damage exposing metal or with substrate damage shall be replaced.

Cleaning and Waste Management:

At completion of each day’s work and at work completion, sweep panels, flashings, and gutters clean. Do not allow fasteners, cuttings, filings, or scraps to accumulate.

Clean exposed surfaces of work promptly after completion of installation.

PROTECTION

Protect Work as required to ensure that roofing will be without damage at Final Completion.

END OF SECTION